## Slide 1
IOT104TC GROUP PROJECT
Smart Classroom
Energy-Saving, Safety
& Asset Monitoring System
A local-first IoT classroom controller with real sensors, real actuators, MQTT operations, dashboard analytics and AI-assisted commands.
UNO Edge Node
Sensors + state machine + actuators
SC2 UART + ACK
ESP32 Gateway
Wi-Fi + MQTT + dashboard command bridge
9+
live hardware signals
5
priority modes
1s
telemetry cadence
432m
recorded evidence
Local safety works even when the network is offline.

## Slide 2
ASSESSMENT FIT
Built around the marking scheme
The demo connects hardware, software, architecture, security/privacy, operations and a practical classroom use-case.
02
Application
A classroom service: save energy, keep comfort and react to safety events.
Architecture
UNO is local authority; ESP32 is gateway; web is operations layer.
Evidence
Telemetry history, dashboard screenshots, live actuators and self-check report.
Security
Local fail-safe control, ignored secrets, browser mic permission and offline state.
Smart Classroom IoT104TC

## Slide 3
USE-CASE
A classroom that reacts locally and reports globally
The system behaves like a small building-management service, not a sensor list.
03
01
Sense
Occupancy, light, temperature, gas, flame and emergency button.
02
Decide
Priority state machine: safety first, then comfort and energy saving.
03
Act
Lamp, relay fan, PWM, tach, buzzer and red-yellow-green status.
04
Operate
MQTT dashboard, manual override, presets, charts and AI timeline.
Safety
highest priority
Comfort
adaptive fan/lamp
Ops
ACK + persistence
Data
charts + history
Smart Classroom IoT104TC

## Slide 4
SYSTEM ARCHITECTURE
Real-time control stays on UNO
Networking adds visibility and commands, but does not become a dependency for safety.
04
Input
Sensors
D2 PIR
A0 Light
A1 Gas
A2 LM35
D8/A3 Flame
D4 Button
Edge
Arduino UNO
millis loop
state machine
relay / PWM / tach
buzzer + status light
Gateway
ESP32
Serial2 UART
Wi-Fi reconnect
MQTT publish
command bridge
Service
Laptop
Mosquitto
web dashboard
history store
AI planner
Design decision: ESP32 is a gateway; UNO remains the controller of record.
Smart Classroom IoT104TC

## Slide 5
HARDWARE EVIDENCE
Dense hardware, clean responsibility
The build is complex, but each module has a clear role in the service.
05
48-kit modules
#18 PIR
#31 TEMT6000
#25 Gas Sensor
#16 Flame Sensor
#5 Active Buzzer
Traffic Light Module
External components
UNO R3
ESP32 Gateway
LM35 powered from ESP32 5V
6-channel relay
12V 4-wire fan
LED + resistor
Wiring rules
Common ground is required.
UNO A5 to ESP32 RX2 uses divider.
Relay logic uses RELAY_ON / RELAY_OFF.
No capacitor is added in this build.
KEY ENGINEERING FIX
LM35 became stable after moving power to ESP32 5V and adding ADC guard compensation.
Smart Classroom IoT104TC

## Slide 6
EDGE INTELLIGENCE
Priority is a state machine
Mixed behavior stays predictable because safety, sensor health, manual control, cooling, lighting and saving are ordered.
06
SAFETY_ALARM
gas/flame/button
SENSOR_ERROR
invalid sensor state
MANUAL
operator override
COOLING
temperature high
LIGHTING
occupied + dark
ENERGY_SAVING
empty or bright
NORMAL
monitoring
WHY IT MATTERS
Dashboard explains what happened and why.
That turns raw telemetry into an operational classroom service.
Smart Classroom IoT104TC

## Slide 7
SAFETY ALARM
The highest-priority path is visible and local
The button gives a safe live demo while gas and flame remain the real sensor paths.
07
Trigger
Three inputs
gasDanger
flameDetected
demoEmergency
Decision
MODE_SAFETY_ALARM
Overrides lighting, cooling and energy-saving logic immediately.
Action
Physical response
red light
pulsed buzzer
fan relay ON
PWM = 255
Demo first: press D4, then watch red light, buzzer pattern, fan response and dashboard alarm.
Smart Classroom IoT104TC

## Slide 8
COMFORT + ENERGY
Human-friendly automation
The classroom avoids waste without making the controls feel abrupt.
08
Lighting
Bright room: lamp stays off even if PIR sees motion.
Dark room + occupied: lamp turns on.
No occupancy timeout: lamp turns off.
Cooling
Temperature threshold starts the relay.
PWM ramps fan intensity.
Tach RPM is interrupt-based and never blocks the system.
10s
occupancy timeout
PWM
smooth fan path
ACK
config confirmed
Local
works offline
Smart Classroom IoT104TC

## Slide 9
MQTT NETWORK LAYER
Telemetry goes up; commands come back with ACK
The protocol is simple enough to debug and structured enough for a dashboard.
09
SC2,mode=SAFETY_ALARM,pir=1,light=323,temp10=286,gas=520,fan=1,pwm=255,rpm=1320,status=R
UNO
Emit
SoftwareSerial line every second
ESP32
Parse
Serial2 + Wi-Fi reconnect
MQTT
Publish
JSON plus key topics
Web
Operate
Config, presets and manual control
ACK loop proves the command actually landed on the UNO.
Smart Classroom IoT104TC

## Slide 10
DASHBOARD
An operator console, not a raw JSON page
Large cards, live charts, mobile access, manual mode and scene presets make the system usable.
10
Auto / Manual
simple operator switch
Presets
one-click scenes
Dashboard screenshots captured from the local running system.

## Slide 11
TELEMETRY EVIDENCE
The demo has history, not just live values
Recorded data supports behavior explanation: modes, temperature response, fan duty and safety events.
11
9,764 samples | avg temp 28.3C | fan duty 31.5% | safety events 5
Smart Classroom IoT104TC

## Slide 12
MEASURED COMPLEXITY
Complexity comes from closed loops
Sensors, control, gateway, dashboard, persistence and AI all interact with the same physical system.
12
9,764
telemetry samples
12+
MQTT topics
2-way
UART command + ACK
Local-first
safety path offline
34/34
delivery self-check PASS
Smart Classroom IoT104TC

## Slide 13
AI OPERATIONS LAYER
Natural language becomes structured control
AI is useful because it turns vague operator intent into ordered tasks and timed actions.
13
Voice
Capture
Browser mic input
STT
Text
faster-whisper
Qwen
Plan
structured tasks
Timeline automation
Example: switch to manual mode in three minutes. Finished tasks clear automatically.
Preference data
Manual overrides become future comfort evidence.
Smart Classroom IoT104TC

## Slide 14
SECURITY, PRIVACY & OPERATIONS
Demo-friendly, but risk-aware
The project separates safety-critical local control from network convenience and AI assistance.
14
Safety boundary
Safety alarm, buzzer, red light and fan response are local on UNO.
Privacy boundary
Microphone is user-triggered and requires browser permission.
Operations boundary
MQTT status, ACK logs, persistence and self-check reduce demo risk.
Production hardening path: authenticated MQTT, TLS, enclosure, fuse, isolation and power filtering.
Smart Classroom IoT104TC

## Slide 15
DEMO CHOREOGRAPHY
Show the strongest engineering first
The audience should see safety and edge control before dashboard polish and AI features.
15
P1
Safety
button -> red light -> buzzer -> fan high
P2
Edge
UNO local controller and priority modes
P3
Energy
PIR + light + temp drive lamp and fan
P4
IoT
UART, MQTT topics and ACK command loop
P5
AI
voice, Qwen, timeline and data preference
Do not open with AI. Open with physical safety response.
Smart Classroom IoT104TC

## Slide 16
REFERENCES + SELF-CHECK
Ready to inspect, rebuild and present
The final package includes sources, assembly materials, scripts and a repeatable delivery check.
16
References
Arduino UNO R3 docs
Espressif Arduino-ESP32 Serial docs
Eclipse Mosquitto config docs
Arduino PubSubClient docs
Texas Instruments LM35 page
Self-check gates
PPT structure
required docs
firmware presence
secret scan
Node/Python syntax
UNO + ESP32 compile
Final claim: a local-first IoT classroom controller with safety, energy saving, operations and evidence-backed intelligence.
Smart Classroom IoT104TC final presentation package